MMX Instructions

Source operands:	mem,MMX reg
Destination operand:	MMX reg
Do not update EFLAGS
MMX instr use letters b(byte), w(word), d(dword), q(qword)	→ with of elements to process

Data transfer instructions:
movd	→ copy dword value
movq	→ copy qword value

Arithmetic instructions:
paddb	→ packed byte addition for specified operands	(dest = dest + source)
paddw	→ same as paddb for word
paddd	→ same as paddb for dword
paddq	→ same as paddb for qword

paddsb	→ packed signed byte addition for specified operands
paddsw→ same as paddsb for word
paddsd	→ same as paddsb for dword
paddsq	→ same as paddsb for qword

paddusb	→ packed unsigned byte addition for specified operands
paddusw	→ same as paddub for word

psubb	→ packed byte subtraction for specified operands	(dest = dest - source)
psubw	→ same as psubb for word
psubd	→ same as psubb for dword
psubq	→ same as psubb for qword

psubsb	→ packed signed byte addition for specified operands
psubsw→ same as paddsb for word

pmaddwd	→ packed signed word multiply with addition for specified operands:
multiplication result of signed words in dest with signed words in source, stored in	temp buffer as signed dwords, then adds two adjacent results together and stores the	results in the destination low and high dword respectively	→ dot product
pmaddubsw→ same as pmaddwd, where dest contains unsigned bytes and source contains signed	bytes, with signed words as temporary results and add of each two adjacent results as	saturated values stored in the destination operand

Comparison instructions:
pcmpeqb	→ packed byte comparison, if EQ destination set to all 1s, otherwise 0s
pcmpeqw	→ same as pcmpeqb, but with words
pcmpeqd	→ same as pcmpeqb, but with dwords
pcmpeqq	→ same as pcmpeqb, but with qwords

pcmpgtb	→ packed signed byte comparison, if destination GT source, destination is set to all	1s, otherwise 0s
pcmpgtw	→ same as pcmpgtb, but with signed words
pcmpgtd	→ same as pcmpgtb, but with signed dwords
pcmpgtq	→ same as pcmpgtb, but with signed qwords